## Slide 1
mpiexec / PMI root
PMI leaf
mcexec
Rank#0
ql_server
ql_mpiexec_start
(1) MPIプロセス起動、標準出力等リダイレクト、MPIプログラムID通知
PMI leaf
mcexec
Rank#N-1
McKernel
ホストLinux
...
(3) 接続
(2) 起動、 MPIプログラム情報登録

## Slide 2
mpiexec / PMI root
PMI leaf
mcexec
Rank#0
ql_server
ql_mpiexec_start
PMI leaf
mcexec
Rank#N-1
McKernel
ホストLinux
(5) 計算完了同期
...
(10) 終了
(4) データ初期化と計算
(6) swap-out
(4)データ初期化と計算
(6) swap-out
(8) swap完了同期
(11) 再開指示待ち
(7) 再開までの処理依頼
(9) 計算完了通知
(7) 再開までの処理依頼
(12) 再開指示待ちバリア参加

## Slide 3
mpiexec / PMI root
PMI leaf
mcexec
Rank#0
ql_server
ql_mpiexec_start
(15) 再開指示、引数、環境変数の記録
PMI leaf
mcexec
Rank#N-1
McKernel
ホストLinux
(18) 再開指示待ちバリア退出
...
(13) 接続・MPIプログラム 情報取得
(17) 再開指示待ちバリア参加・退出
(20) swap-in
(21) 再開指示、引数、環境変数取得
(22) データ再初期化
(23) 計算
(14) 標準出力等 リダイレクト 再開
(20) swap-in
(21) 再開指示、引数、環境変数取得
(22) データ再初期化
(23) 計算
(16) 再開指示
(19) McKernelへの制御復帰
(19) McKernelへの制御復帰

## Slide 4
mpiexec / PMI root
PMI leaf
mcexec
Rank#0
ql_server
ql_mpiexec_finalize
(4) 終了指示
PMI leaf
mcexec
Rank#N-1
McKernel
ホストLinux
(6) 再開指示待ちバリア退出
...
(1) 接続・MPIプログラム 情報取得
(5) 再開指示待ちバリア参加・退出
(11) MPIプログラム 削除
(3) 終了指示の記録
(8) swap-in
(9) 終了指示取得
(10) 終了
(2) 標準入出力等 リダイレクト 再開
(7) システムコールからの復帰
(7) システムコールからの復帰
(8) swap-in
(9) 終了指示取得
(10) 終了

## Slide 5
ホストOS
mcexec
プロセス
kill システムコール
tty
^C
シグナル
シグナル
McKernel
シグナル処理
スレッド
システムコール処理スレッド
シグナル
シグナル受信プロセス
Page
Fault
GPF
プロセス
kill システムコール
シグナル
シグナル
シグナル
McKernel シグナル処理
IKC通信
SIGALRM
SIGPIPE
など
子プロセス
終了

## Slide 6
McKernel
mcexec
シグナルハンドラ
シグナル
シグナル登録処理
(do_kill)
IKC受信処理
（任意のシグナル）
GPF割り込みハンドラ
（SIGILL)
Page Fault割り込みハンドラ（SIGBUS、SIGSEGV)
kill系システムコール
（任意のシグナル）
プロセス終了処理
（SIGCHLD)
IKC
process
構造体
sig_pending
構造体
登録
参照
シグナルチェック処理
(check_signal)

## Slide 7
Partition2
IHK-Slave1
Core
McKernel1
Core
・・・
Core
Core
・・・
IHK-Slaven
McKerneln
・・・
Linux
Core
Core
・・・
mcexec1
mcctl
IHK-Master
mcexecn
・・・
Partition1
Partitionn+1
・・・
User space
Kernel space

## Slide 8: 1 Background
MPI communication on receiver side
Post receive command into local queue
  The command has matching tag, buffer address, pointer to MPI-request structure on which the completion of the receive is marked
(Sender side sends packet to responder)
Monitor packet arrival by polling NW-HW event queue or message body repeatedly
Detect packet arrival, find matching command in the local queue, copy payload to final buffer and then mark the completion
Compute-Core
OS-core
3
1
4
a
Steps 3-4 can be performed by another thread (called MPI progress thread) to parallelize the receive
Run it on OS-core to make use of the less busy core
Compute-Core
Post recv command
3
Monitor packet arrival
1
4
Tag-match, copy and mark
a
Computation
4'
Check the mark
Speedup

## Slide 9: 2.1 Interfaces and steps
Process on McKernel specifies a core by using pthread_attr_setaffinity_np() (modify pthreads or prepare a new function with similar interface)
  McKernel assigns numbers to OS-cores as well so that it can specify them
It specifies instruction address by using pthread_create() (modify pthreads or prepare a new function with similar interface)
McKernel detects an OS-core is specified, communicate with mcexec, mcexec generates a thread by using pthread_create()
McKernel
Linux
OS core
OS core
Compute core
Compute core
IHK−slave
(S3)
(S1)
mcexec
Thread
IHK−master

## Slide 10: 2.2 Memory Management
Virtual address space
Stack for OS core thread
Text for OS core thread
data
bss
text
Stack
mmap
Provide proper view of segments to the thread
  text, data, bss, mmap segments  OS-core thread can use the same addresses as the parent McKernel process because it's a child thread of mcexec and address space are shared among mcexec and the McKernel process
  stack  Reserve part of virtual memory area of McKernel process and make McKernel page-fault handler handle the area as the legal area so that the area can be used for stack by the OS-core thread
(M1)
(M2)
heap

## Slide 11
Linux
Core
Core
・・・
IHK-Master
Partition1

## Slide 12
Core
McKernel1
Core
・・・
Core
Core
・・・
McKerneln-1
・・・
Linux
Core
Core
・・・

## Slide 13
PartitionM+1
Partition3
Partition2
Partition1
PartitionN+1
Partition3
Partition2
Partition1
McKernel1
Linux
Core
Core
・・・
Core
Core
・・・
(1) One Linux partition + One McKernel partition
(3) One Linux partition + N McKernel partitions on N cache coherency domains for N jobs
McKernel1
Linux
Core
Core
・・・
Core
Core
・・・
Cache coherency domain1
McKernel2
Core
Core
・・・
Domain2
McKernelN
Core
Core
・・・
DomainN
・・・
McKernel1
Linux
Core
Core
・・・
Core
Core
・・・
Job1
(2) One Linux partition + M McKernel partitions for M jobs
McKernelM
Core
Core
・・・
McKernel2
Core
Core
・・・
・・・
Partition1
Partition2
・・・
JobM
Job2
Job1
・・・
JobN
Job2

## Slide 14
ユーザが〈McKernel動作モード，タイマ割り込み不使用カーネル〉 のジョブを投入するジョブキュー（システムはノードをMcKernelモードにする）
ユーザが〈McKernel動作モード，PVASカーネル〉 のジョブを投入するジョブキュー（システムはノードをMcKernelモードにする）
ユーザが〈McKernel動作モード，高速起動メモリスナップショットカーネル〉 のジョブを投入するジョブキュー（システムはノードをMcKernelモードにする）
ユーザがLinux動作モードのジョブを投入するジョブキュー （システムはノードをLinuxオンリーモードにする）
ジョブスクリプトに動作モード及びカーネル種類が指定されていればその設定を用い、 指定されていなければデフォルト設定を用いるジョブキュー
＊ジョブスクリプトに指定されている動作モード及びカーネル種類が ジョブキューが想定するものと異なっている場合はエラー

## Slide 15
管理用 ネットワーク （Ethernet）
データ転送用 ネットワーク （IB）
計算ノード
・・・
論理コア１
名前解決用データ
シャーシ＃2
シャーシ＃5
IBを持つノード
計算ノード
計算ノード
・・・
12ノード×18シャーシ×602
・・・
論理コアNcore
論理コア１

## Slide 16
統計情報 ユーザCPU使用時間(積算値) システムCPU使用時間(積算値) 使用CPU数(現在値) 使用CPU数(最大値) 物理メモリ使用値(現在値) 物理メモリ使用値(最大値) スワップ使用量(現在値) スワップ使用量(最大値) 仮想メモリ使用値(現在値) 仮想メモリ使用値(最大値) リードシステムコール要求量(積算値) ライトシステムコール要求量(積算値) リードシステムコール数(積算値) ライトシステムコール数(積算値) ファイルシステムに対するリード量(積算値) ファイルシステムに対するライト量(積算値) ファイルシステムに対するリード要求数(積算値) ファイルシステムに対するライト要求数(積算値)

## Slide 17
統計情報 | 記録方法とそのタイミング | 取得・提示方法とそのタイミング
ユーザCPU使用時間 (積算値) | McKernelがプロセス実行中に記録。子孫プロセス合算値はmcexecがプロセス生成消滅時に記録。 | mcexecがプロセス終了時にprocfsで取得しカーネルモジュールを経てジョブスケジューラに提示
システムCPU使用時間(積算値) |  | 
使用CPU数(現在値) | McKernelがプロセス実行中に記録。 | ジョブスケジューラがプロセス実行中にカーネルモジュール経由でprocfsで取得。
使用CPU数(最大値) | McKernelがプロセス実行中に記録。 | mcexecがプロセス終了時にmcctl経由で取得しカーネルモジュール経由でジョブスケジューラに提示。
物理メモリ使用値 (現在値) | McKernelがプロセス実行中に記録。 | mcexecがプロセス終了時にprocfsで取得しカーネルモジュール経由でジョブスケジューラに提示。 スワップは使用しないためゼロを提示。
物理メモリ使用値 (最大値) |  | 
スワップ使用量(現在値) |  | 
スワップ使用量(最大値) |  | 
仮想メモリ使用値(現在値) |  | 
仮想メモリ使用値(最大値) |  | 
リードシステムコール要求量(積算値) | Linuxがプロセス実行中に記録。 | mcexecがプロセス終了時にTaskstatsまたはSystemTapで取得しカーネルモジュール経由でジョブスケジューラに提示。
ライトシステムコール要求量(積算値) |  | 
リードシステムコール数(積算値) |  | 
ライトシステムコール数(積算値) |  | 
ファイルシステムに対するリード量(積算値) | Linuxのドライバあるいはファイルシステムのクライアントがファイルシステムごとにプロセス実行中に記録。 | mcexec/mcctrlがプロセス終了時に拡張procfsで取得しカーネルモジュール経由でジョブスケジューラに提示。
ファイルシステムに対するライト量(積算値) |  | 
ファイルシステムに対するリード要求数(積算値) |  | 
ファイルシステムに対するライト要求数(積算値) |  | 

## Slide 18
統計情報 | 記録方法とそのタイミング | 提示／取得方法とそのタイミング
ユーザCPU使用時間 (積算値) | McKernelがプロセス実行中に記録。子孫プロセス合算値はmcexecがプロセス生成消滅時に記録。 | ジョブスケジューラがプロセス実行中にprocfsで取得。またはmcexec/mcctrlがプロセス終了時にprocfsで取得しファイルまたは標準出力でジョブスケジューラに提示。子孫合算値はmcexecがプロセス終了時にファイルまたは標準出力でジョブスケジューラに提示。
システムCPU使用時間(積算値) |  | 
使用CPU数(現在値) | McKernelがプロセス実行中に記録。 | ジョブスケジューラがプロセス実行中にprocfsで取得。
使用CPU数(最大値) | McKernelがプロセス実行中に記録。 | ジョブスケジューラが拡張procfsインターフェイスで取得。
物理メモリ使用値 (現在値) | McKernelがプロセス実行中に記録。 | ジョブスケジューラがprocfsインターフェイスで取得。またはmcexec/mcctrlがプロセス終了時にprocfsで取得し標準出力でジョブスケジューラに提示。 スワップは使用しないためゼロを提示。
物理メモリ使用値 (最大値) |  | 
スワップ使用量(現在値) |  | 
スワップ使用量(最大値) |  | 
仮想メモリ使用値(現在値) |  | 
仮想メモリ使用値(最大値) |  | 
リードシステムコール要求量(積算値) | Linuxがプロセス実行中に記録。 | ジョブスケジューラがプロセス実行時にTaskstatsまたはSystemTapで取得。またはmcexec/mcctrlがプロセス終了時にTaskstatsまたはSystemTapで取得しファイルまたは標準出力でジョブスケジューラに提示。
ライトシステムコール要求量(積算値) |  | 
リードシステムコール数(積算値) |  | 
ライトシステムコール数(積算値) |  | 
ファイルシステムに対するリード量(積算値) | Linuxのドライバあるいはファイルシステムのクライアントがファイルシステムごとにプロセス実行中に記録。 | ジョブスケジューラが拡張procfsインターフェイスで取得。またはmcexec/mcctrlがプロセス終了時に拡張procfsで取得しファイルまたは標準出力でジョブスケジューラに提示。
ファイルシステムに対するライト量(積算値) |  | 
ファイルシステムに対するリード要求数(積算値) |  | 
ファイルシステムに対するライト要求数(積算値) |  | 

## Slide 19
エントリ | 使用が確認されたアプリやライブラリ
/proc/stat | Intel OpenMP run-time
/proc/<pid>/tasks/<tid>/stat | gdb
/proc/<pid>/mem | gdb
/proc/<pid>/aux | gdb
/proc/<pid>/pagemap | LTP
/sys/devices/system/cpu/online | Intel OpenMP run-time (attached configuration)

## Slide 20
 | Implemented | Planned
Process Thread | arch_prctl, clone, execve, exit, exit_group, fork, futex, get_cpu_id, getpid, get{u,g}id, gete{u,g}id, getres{u,g}id, getppid, gettid, kill, pause, ptrace, rt_sigaction, rt_sigpending, rt_sigprocmask, rt_sigqueueinfo, rt_sigreturn, rt_sigsuspend, set_tid_address, set{u,g}id, setre{u,g}id, setres{u,g}id, setfs{u,g}id, setpgid, sigaltstack, tgkill, vfork, wait4, waittid | {get,set}rlimit, {get,set}_thread_area, rt_sigtimedwait, signalfd, signalfd4
Memory Mgmt. | brk, madvise, mincore, mlock, mmap, mprotect, mremap, msync, munlock, munmap, process_vm_{readv,writev}, remap_file_pages, set_robust_list, shmat, shmctl, shmdt, shmget | {get,set}_mempolicy, {get,set}_robust_list, mbind, migrate_pages, mlockall, modify_ldt, move_pages, munlockall
Scheduling | getcpu, gettimeofday, nanosleep, sched_getaffinity, sched_setaffinity, sched_yield | alarm, {get,set}itimer, settimeofday, time, times
Perf. Counter | Original functions: pmc_init, pmc_start, pmc_stop, pmc_reset | PAPI functions

## Slide 21
Linux
Cores1
Coree1
・・・
IHK-master
IHK-kernel-module
mcexec
mcctl
McKernel
Cores1
Coree1
・・・
IHK-Slave
IHK-Slave1

## Slide 22
ihk
├── cokernel IHK-slave module
│ ├── attached Files for Host processor plus PCI-Attached Co-processor
│ │ │ configuration
│ │ └── mic Files for Intel Xeon Phi processor
│ │ └── include
│ │ └── ihk
│ └── smp Files for SMP processor only configuration
│ └── x86 Files for Intel Architecture processor
│ └── include
│ └── ihk
├── doxygen
├── ikc IKC functions to be included in IHK-master and IHK-slave
│ └── include
│ └── ikc
├── include
│ └── sysdeps
│ └── mic
│ └── mic
├── linux IHK-master module
│ ├── core
│ │ └── ikc -> ../../ikc
│ ├── driver Linux kernel module part
│ │ ├── attached Files for Host processor plus PCI-Attached Co-processor
│ │ │ │ configuration
│ │ │ └── mic Files for Intel Xeon Phi processor
│ │ └── smp-x86 Files for SMP processor only configuration
│ │ Files for Intel Architecture processor
│ │
│ ├── include
│ │ └── ihk
│ │ └── misc
│ └── user User interface for IHK-master
└── test

## Slide 23
mckernel
├── arch Processor architecture dependent part of kernel functions
│ └── x86 Files for Intel 64 architecture
│ ├── elfboot ELF loader prepended to Kernel image for attached configuration
│ ├── kboot Kernel page preparation and ELF loader code prepended to Kernel
│ │ image for SMP processor only configuration
│ ├── kernel Kernel functions
│ │ └── include
│ │ └── ihk
│ └── tools Scripts to boot/reboot/shutdown McKernel
├── doxygen
├── executer
│ ├── include
│ ├── kernel Delegator module (mcctrl)
│ └── user Proxy process (mcexec)
├── kernel Processor architecture independent functions
│ ├── config
│ ├── include
│ │ └── lwk
│ └── script Scripts for creating a kernel image
├── lib Utility functions for kernel
│ └── include
│ └── ihk
└── test

## Slide 24
Category Implemented(*1) Planned
===============================================================
Process arch_prctl get_thread_area
Thread clone getrlimit
execve ptrace
exit rt_sigtimedwait
exit_group set_thread_area
futex setrlimit
getpid signalfd
getrlimit(*2) signalfd4
kill
pause
ptrace(*2)
rt_sigaction
rt_sigpending
rt_sigprocmask
rt_sigqueueinfo
rt_sigreturn
rt_sigsuspend
set_tid_address
setpgid
sigaltstack
tgkill
vfork
wait4
---------------------------------------------------------------
Memory brk get_robust_list
Management gettid mincore
madvise mlockall
mlock modify_ldt
mmap munlockall
mprotect set_robust_list
mremap shmat
munlock shmctl
munmap shmdt
remap_file_pages shmget
process_vm_readv
process_vm_writev
---------------------------------------------------------------
Scheduling sched_getaffinity alarm(*3)
sched_setaffinity getitimer(*3)
gettimeofday(*3)
nanosleep(*3)
sched_yield
setitimer(*3)
settimeofday(*3)
time(*3)
times(*3)
---------------------------------------------------------------
Performance Original Interface: PAPI Interface
Counter pmc_init
pmc_reset
pmc_start
pmc_stop
---------------------------------------------------------------
Other Kernel /proc and /sys Filesystem
Functions Large Page Interface
cgroups
---------------------------------------------------------------
*1: System calls not listed below are delegated to Linux.
*2: Some functions have not been implemented.
*3: These system calls are delegated to Linux for the moment.

## Slide 25
linux/
|--- 3.0/
|--- aal/ => symbolic link to ../../aal/host/linux
aal/
|--- host/
| |--- driver/
| | |--- knf/
| | |--- mee/
| |--- linux/
|
|--- ikc/
|--- include/
| |--- sysdeps/
| |--- knf/
|--- manycore/
|--- generic/
|--- knf/
|--- mee/
|--- x86_common

## Slide 26
|--- include/aal/
| |--- aal_host_driver.h Definitions for AAL-Host I/F
| |--- aal_host_misc.h Page allocator, etc.
| |--- aal_host_user.h ioctl requests definition
| |--- ikc.h includes IKC headers
| |--- misc/debug.h dprintf -> printk, etc.
|
|--- linux/
| |--- host_driver.c Character devices for Linux
| |--- host_linux.h Definition in Linux
| |--- mem_alloc.c Allocator
| |--- mikc.c IKC master channel creator
| |--- mm.c Under construction
| |--- ops_wrappers.h ops wrapper functions
(cont.)

## Slide 27
|--- generic/ Generic (Architecture-independent)
| |--- include/ Header files (generic)
| |--- aal/ AAL Stuffs
|
|--- x86_common/ Common files in the x86 architecture
| |--- include/
| |--- aal/
|
|--- knf/ Knights Ferry files
| |--- include/
| |--- aal/
|
|--- mee/ MEE files
| |--- include/
| |--- aal/
|

## Slide 28
core
core
core
core
…
core
…
………....
core
core
core
core
…
core
…
………....
core
core
core
core
…
core
…
………....
core
core
core
core
…
core
…
………....
core
core
core
core
…
core
…
………....
core
core
core
core
…
core
…
………....
2 NUMA nodes
4 NUMA nodes
8 NUMA nodes
Many NUMA nodes

## Slide 29
core
core
core
core
…
core
…
………....
Micro Kernel
Linux Kernel
Linux Adaptation Layer
User
Process
core
core
core
core
…
core
…
………....
Linux Kernel
Light-Weight
Kernel
User
Process
core
core
core
core
…
core
…
………....
Linux Kernel
Interrupt forwarder
User
Process
a) Traditional Micro Kernel Approach
b) Linux + User Process on Light-Weight Kernel
c) Linux + User Process on interrupt forwarder

## Slide 30
Many Core
Cores for Linux
Application Cores
Dedicated OS service Cores
Interconnect
McKernel
IHK-cokernel
IHK-IKC
Linux API (glibc)
MPI
PGAS
OpenMP
Linux Kernel
IHK-Linux driver
IHK-IKC
mcctrl
mcexec
Helper Threads
McKernel
IHK-cokernel
IHK-IKC

## Slide 31
$ mcexec ./a.out
$ mcexec ./a.out
Regular a.out process
in Linux
text, data, bss
mmap area
stack
0000000000000000
00007fffffffffff
Ffff800000000000
fffffffffff00000
a.out process
in McKernel
mcexec Process
in Linux
text, data, bss
mmap area
Hole
Hole
Stack
McKernel Space
mmap area
tｅｘt, data, bss
stack
Linux Kernel Space
0000000000000000
00007fffffffffff
Ffff800000000000
fffffffffff00000
phys mem. on app. cores
phys mem. on Linux cores
Memory mapped area is allocated in Xeon Phi physical memory and shared by both processes
The mcexec program is compiled with options -fPIE -pie
The mcexec binary is loaded in the different address than the regular a.out binary
It creates an a.out process in McKernel
The a.out user virtual memory space in McKernel is shared by the same address space in the mcexec process.

## Slide 32
Job submission queues
(1) Boot with Linux and wait for a job
(3) Remove McKernel and wait for a job
Launch McKernel and run app A on it
Done
Launch McKernel with local data store and run app C on it
(2) Launch McKernel with large page optimization and run app B on it
Run app D on Linux
Done
McKernel-default
McKernel-large-page
…
McKernel-local-data-store
Linux
Memory
IHK-Slave
IHK-Master
Delegator module
Proxy process
core
core
core
core
…
…
McKernel
Linux
Application
Partition
Partition
Daemon
Memory
IHK-Slave
IHK-Master
Delegator module
Proxy process
core
core
core
core
…
…
McKernel
Linux
Application
Partition
Partition
Daemon
Memory
IHK-Slave
IHK-Master
Delegator module
Proxy process
core
core
core
core
…
…
McKernel
Linux
Application
Partition
Partition
Daemon
Memory
IHK-Master
Delegator module
core
core
core
core
…
…
Linux
Application
Partition
Daemon
Memory
IHK-Master
Delegator module
core
core
core
core
…
…
Linux
Partition
Daemon
Launch
Launch
Launch
Done
Launch
Done

## Slide 33
実行カーネルの指定とジョブの優先順位および計算ノードは連動しない
ジョブキューによる指定
  ジョブキュー毎に実行するカーネルを紐づける
  ジョブキューが指定できるが実際には、キュー自体は仮想的なものでジョブに属性を付けるだけという実装もありだろう
ジョブスクリプトによる指定
  新たにスクリプトコマンドおよびコマンドオプション
McKernel-nosched用ジョブキュー
McKernel-sched用ジョブキュー
MvKernel-PVAS用ジョブキュー
Linux-only用ジョブキュー
defaultジョブキュー
ジョブスクリプトで指定されていなければ、default configuration.
ジョブスクリプトで指定されていれば、指定configuration.
ジョブスクリプトで指定されているconfigurationでないジョブキューに投入したらエラー

## Slide 34
Virtual address space of mcexec
Virtual address space of McKernel process
Physical
memory
mcexec mmap
Not used
App heap
App mmap
App text
[mckernel]
[mckernel]
File in Linux
(1) mcctrl creates a file and mmap it in a way that mcctrl can capture page faults occurring on the VM areas of McKernel process
(2) mcctrl asks McKernel to obtain physical page if needed and then copy page table entry of McKernel process to page table of mcexec
mcexec text
mcexec heap
mcexec stack
App stack
App data/bss
mcexec data/bss

## Slide 35
View of struct representing VM area of mcexec in Linux
View of struct representing VM area of McKernel process
Proxy process
text, data etc.
Not used
Heap
Anonymous mapping etc.
App text, data etc.
[mckernel]
[mckernel]
File in Linux

## Slide 36
Virtual address space of mcexec in Linux
Virtual address space of app in McKernel
Physical
memory
Proxy process
text, data etc.
Not used
Heap
Anonymous mapping etc.
App text, data etc.
[mckernel]
[mckernel]
File in Linux

## Slide 37: anon_inode_getfile
IHK-Slave
Linux
IHK-Master
Node Monitor Daemon
Report resource full
User space
Kernel space
Process
mcctrl
Virtual memory area
Virtual address space

## Slide 38
address
space
process
runq, current
thread
CLV
process_vm
page_table
vm_regions
vm_ranges
vm_ranges
vm_ranges
thread
thread
CLV
CLV
thread
hash
process
hash
process
process
process
children
parent
thread
thread
thread
process_vm
resource
set
CPU
set
phys mem
set

## Slide 39
Linux提供 procfs/sysfs
procfs/sysfs
フレームワーク
procfs/sysfs
フレームワーク
アプリケーション
プログラム
McKernel提供procfs/sysfs
Linux
McKernel
mcoverlayファイルシステム
mcctrl
(1) open()などによる アクセス
(4) アクセス要求転送
(3) コールバック関数呼び出し
mcexec
(2) McKernel提供ファイルまたは Linux提供ファイルへの振り分け

## Slide 40
Memory
IHK Linux
Delegator module
CPU
CPU
CPU
CPU
…
…
McKernel
Linux
System daemon
Kernel daemon
Proxy process
IHK Co-kernel
HPC Application
Interrupt
System call
System call
Partition
Partition
OS jitter contained in Linux, LWK is isolated

## Slide 41
Memory
IHK-Master
Delegator module
core
core
core
core
…
…
McKernel
Linux
System daemon
Kernel daemon
Proxy process
IHK-Slave
Application
Interrupt
System call
System call
Partition
Partition
OS noise contained in Linux, isolated from McKernel
Performance sensitive system calls are implemented in McKernel, others are offloaded to Linux

## Slide 42
Root-task text/data/BSS
Shared heap
Shared mmap
Shared object linked to task#1 text/data/BSS
Task#1 text/data/BSS
Task#1 stack
Shared object linked to Task#0 text/data/BSS
Task#0 text/data/BSS
Task#0 stack
Root-task stack
Kernel
0x 0000 0000 0000 0000
0x ffff ffff ffff ffff